Meteorologic and Hydrologic Data Sets for the North

Slope of Alaska along the Kuparuk River Watershed

1985-2007

Douglas L. Kane, Robert E. Gieck Jr., Larry D. Hinzman

and Elizabeth K. Lilly

Water Research Center

Institute of Northern Engineering

University of Alaska Fairbanks

Fairbanks, Alaska  99775-5860

# UPDATED 01/04/07

reg

Principal Investigators Information

Douglas Kane

University of Alaska Fairbanks
Institute of Northern Engineering
Water and Environmental Research Center
P.O. Box 755860
Fairbanks, Alaska 99775-5860 U.S.A.

Phone 1-907-474-7808
Fax 1-907-474-7979
e-mail ffdlk@uaf.edu
web <http://www.uaf.edu/water/>http://www.uaf.edu/water/

Larry D. Hinzman

University of Alaska Fairbanks
International Arctic Research Center

P.O. Box 757340
Fairbanks, Alaska 99775-5860 U.S.A.

Phone 1-907-474-7331
Fax 1-907-474-7979
e-mail ffldh@uaf.edu

### FUNDING AGENCIES

U.S. Department of Energy’s Office of Health and Environmental Research , Ecological Research Division, R4D Program in Arctic Tussock Tundra.

National Science Foundation Grants:

OPP-9318535, OPP-9214927 and OPP-9814984

INTRODUCTION

Various research projects on the North Slope of Alaska have, since the mid 1980's, resulted in the establishment of several unmanned meteorological and research sites on a north-south transect.  For logistical reasons, all of the present sites are located along the Dalton Highway or accessible from roads on the Prudhoe Bay oil field.  The catalyst for this data collection program was the Department of Energy's R4D project at Imnavait creek where the first meteorological data sites were established in 1985 and 1986.  One year later in 1987, additional meteorological sites were established at Sagwon and Franklin Bluffs.

In 1992, another meteorological site was installed in conjunction with a wetlands study funded by the U.S. Geological Survey on the west side of the Prudhoe Bay oil field on the banks of the Kuparuk River.  In 1993, the Imnavait Basin A site was moved several kilometers, renamed, and re-installed on the Kuparuk River south of the Dalton Highway near Toolik Lake.  Finally, in 1994, the first remote meteorological station that transmits via satellite was installed on the Kuparuk River 90 km south of the Arctic Coast in the western most part of the Kuparuk River Basin.  No data are reported for either the Upper or West Kuparuk stations in this report.

The quality and continuous collection of this data is only possible because of the availability of solid state instrumentation and data loggers.  The quality of most data is very good, although some instrumentation does not work well for various environmental conditions.  For example, precipitation gages do not work well in windy conditions and radiometers do not work well when coated with rime ice, condensation, dust, etc..  We have tried to identify bad data and remove it, but this is not always possible.  Because of poor performance during the winter months, we do not collect data from radiometers and the standard 8 inch (20 cm) orifice precipitation gages from September through mid-April.

The collection of this data set would not be possible without the support of the Department of Energy, U.S. Geological Survey and the National Science Foundation.  We would also like to thank the many individuals who assisted us over the years in the collection of this data.

## SITE DESCRIPTION

On Alaska's North Slope, starting in 1985, meteorological stations at various research sites were located in a north-south transect along the Dalton Highway (figure 1 -- postscript file FIGURE1.PS).  The southernmost site was established in the foothills of the Philip Smith Mountains at the headwaters of Imnavait Creek (latitude 68 degrees, 37 minutes N, longitude 149 degrees, 17 minutes W).  This watershed has an average elevation of 910 m and is located 165 km south of Prudhoe Bay and 15 km north of the Brooks Range.  The most intense research and data collection have occurred at this location.  A typical meteorological station is shown in figure 2.

Figure 1.  North Slope Site Locations

Instrumentation for the collection of meteorologic, hydrologic and soil conditions was installed in 1984 and data collection began in the spring of 1985.  The hydrology, meteorology and ecology of this watershed have been studied extensively (Everett and Ostendorf, 1988; Hinzman et al., 1991; Hinzman and Kane, 1991; Hinzman et al., 1992; Kane and Hinzman, 1988; Kane et al., 1989;   Kane et al., 1990; Kane et al., 1991a; Kane et al., 1991b; Walker et al., 1989).

Figure 2.  Kuparuk Basin Meteorological

In the Imnavait Watershed there are two main sites where data collection has taken place.  One site, Imnavait A site is located on a 10% west-facing slope, the other site, Imnavait B site is located on a ridge top on the east side of Imnavait Creek Watershed.  Meteorologic and soil information were measured at both locations. Near Imnavait A site four runoff plots were constructed in a transect along the slope.  These sites were named Imnavait D site (plot 1, upper slope), Imnavait E site (plot 2, upper mid-slope), Imnavait F site (plot 3, lower mid-slope) and Imnavait G site (plot 4, lower slope).  Snow and soil temperature profiles were measured adjacent to each runoff plot.  Heat flux and precipitation were also measured at Imnavait C site, located midway between Imnavait F and G sites.  Imnavait H site was established near the outlet of the basin to measure stream flow.  Imnavait W site, otherwise known as the USDA Soil Conservation Service Toolik River Site, is a Wyoming snow gage located near Imnavait B site.  Imnavait S site was established as a snow survey transect paralleling the slope next to Imnavait sites D, E, F and G (runoff plots) and running from the east boundary across the watershed to the west boundary.

The mineral soils in this area are cold, wet, poorly drained silt loams with a high organic content and include many glacial erratics of various sizes.  The mineral soils are covered by a peaty layer, and are classified as Histic Pergelic Cryaquepts (Rieger et al., 1979).  The vegetation is mostly water tolerant plants   such as tussock sedges and mosses, but there are also lichens and shrubs such as willows, alder and dwarf birch.  More complete descriptions of tundra vegetation have been published (Brown and Berg, 1980; Walker et al., 1989).  The area was glaciated during the Pleistocene and is underlain by continuous   permafrost.  The maximum thaw depth during the period of study was approximately 120 cm, with typical depths being 40 cm.

In 1986, a second site was established near the Sagwon Bluffs (latitude 69 degrees, 25 minutes N, longitude 148 degrees, 45 minutes W) approximately  100 km south of Prudhoe Bay.  This site is located in a transitional zone between costal plain and the foothills at an elevation of 370 m.  The vegetation is also characteristic of tussok tundra and the soils are loamy with a peaty surface layer and are poorly drained (Everett, 1980).  Instrumentation for measuring soil temperatures and meteorologic conditions as installed near the top of a 10% north-facing slope.  Data have been collected for 7 years (1987-1993) at this site.

Also in 1986, a site near Franklin Bluffs (latitude 69 degrees, 50 minutes N, longitude 148 degrees, 45 minutes W) was established on the costal plain 50 km south of Prudhoe Bay.  This site is located in the relatively flat area of the Sagavanirktok River flood plain at an elevation of 80 m.  The vegetation is comprised of a continuous cover of grasses and sedges rooted in mosses and lichens (Komarkova and Webber, 1980).  The soils are poorly drained and generally do not thaw to depths of more than 50 cm.  Organic materials of variable thickness overlie silt-loam textured mineral soils (Everett, 1980).  Data have been collected for 7 years (1987-1993) at this site.

The northernmost site was established 21 km west of Deadhorse on the banks of the Kuparuk River (latitude 70 degrees, 17 minutes N, longitude 148 degrees, 58 minutes W).  This site is located in an area with little topographic relief at an elevation of 50 m.  The vegetation consists of wet sedge tundra and forb tundra.  The soils are organic overlying layers of fine sand and silts.  This site was established in April of 1992.

## FILE AND DATA FORMATS

Data were compiled and tabulated in annual data sets for each site.  These data were further subdivided into data sets of various types: meteorological, radiation, soil temperature and heat flux, stream flow and snow surveys.  The first two characters in the file name specify the site name, the next four   characters identify the year of the record, the final letters describe the general type of data.  The codes for the site names, year and data types are shown in Table 1.  A full listing of files by site name is given in Tables 2a and 2b.  The files are in comma separated ASCII format.  Some examples of file names are:

IB1987M.DAT     1987 Imnavait B site meteorological data

SH1992T.DAT     1992 Sagwon soil temperature data

FB1990R.DAT     1990 Franklin Bluffs radiation data

IH1991Q.DAT     1991 Imnavait Creek stream flow

IC1987T.DAT     1987 Imnavait C site heat flux and soil temperatures

Each file begins with several lines identifying the site, year of record and general type of data within the data set.  Following this, specific data columns are identified.  Data are generally hourly or daily average values.  However, some data such as stream flow and snow water equivalent are point values taken at varying time periods.  Hourly average values represent the average conditions during the hour proceeding the given time.

Daily average values represent average conditions for the given day beginning at one minute past midnight and ending at midnight.  All dates and times are in Alaska Standard Time.

INSTRUMENTATION SPECIFICATIONS

DATA LOGGERS, CABLES AND MOUNTS

Campbell Scientific 21X and CR10X data loggers were used to record and process data at all sites.  Data recorded on the data loggers were compared to measured conditions to check the sensor calibrations and the data logger during site visits.  Cables connecting the sensors to the data logger were shielded to minimize induced voltage caused by auroral activity.  Heavy flexible metal conduit was used at some sites to discourage wildlife. Tripod masts (3 m) were used to mount sensors at Imnavait A site, Sagwon and Franklin Bluffs sites.  At Imnavait B site, a 10 meter meteorological tower was used to mount the air temperature, relative humidity, wind speed and direction sensors.  Radiation sensors were mounted on a separate tripod mount design to suspend this sensor over the tundra and minimize shadows.  A 3 meter tower was used to mount the sensors at the Lower Kuparuk site.

Some of the longer outages in the data sets are due to damage caused by wildlife.  Bears have been attracted to the sites and caused severe damage.  Moose and caribou have damaged cables with their hooves and by rubbing on the towers.  Smaller wildlife, rodents and foxes, have also gnawed cables causing outages.  The severity of the weather encountered at these sites has also taken its toll on the instrumentation.  Lightning and prolonged extreme cold have damaged data loggers and batteries causing outages.

Table 1. File name formats.

FILE IDENTIFICATION FORMATS

_________________________________________________________________________

FIRST TWO CHARACTERS             | YEAR         | FINAL CHARACTER

Site Identification              |              | Data Type(s)

_________________________________|______________|________________________

BM   Betty Pingo    (replaces LK)| 1994-present |

FB   Franklin Bluffs Site        | 1986-pres    |

GL   Green Cabin Lake Site       | 1996-pres    |

IA   Imnavait A Site             | 1985-1992    | M   Meteorological

IB   Imnavait B Site             | 1986-pres    | Q   Stream Discharge

IC   Imnavait C Site             | 1985-1992    | R   Radiation

ID   Imnavait D Site             | 1985-1992    | S   Snow Surveys

IE   Imnavait E Site             | 1985-1992    | T   SoilTemperatures

IF   Imnavait F Site             | 1985-1992    |(includes soil heat flux

IG   Imnavait G Site             | 1985-1992    | at Imnavait C site)

IH   Imnavait Flume              | 1986-pres    |

IS   Imnavait Snow Course        | 1985-1992    |

IR   Imnavait Ridge Site         | 1993-pres    |

IV   Imnavait Valley Site        | 1993-pres    |

IW   Imnavait Wyoming snow gage  | 1985-1992    |

LK   Lower Kuparuk Site          | 1992-1995    |

NH   North Headwater             | 1996-pres    |

SH   Sagwon site                 | 1986-pres    |

SW   Sagwon Wyoming snow gage    | 1986-1992    |

UH   Upper Headwater             | 1996-pres    |

UK   Upper Kuparuk site          | 1993-pres    |

WD   West Dock                   | 1995-pres    |

WH   West Headwater              | 1996-pres    |

WD   West Kuparuk Site           | 1995-pres    |

_________________________________|______________|________________________

## WIND SPEED AND DIRECTION

Wind speed was measured using a Weathertronics anemometer at Imnavait A site from 1985 through 1992.  The threshold of the wind measurement is 0.22 m/s and the accuracy is plus/minus 0.07 m/s.  Met One model 014A wind speed sensors were employed at Imnavait B site, Sagwon, Franklin Bluffs and Lower Kuparuk sites.  The threshold velocity of this instrument is rated at 0.447 m/s and the reported accuracy is approximately 0.1 m/s.  Beginning in 2006 the all the 10 meter wind speed and direction sensors and most 3 meter sensors were replaced with RM Young aero-vanes.  This  Field calibration tests of the wind speed sensors are difficult to obtain, sensors are regularly replaced and sent to the manufacturer for calibration and replacement of bearings.  Wind direction was measured with a model 024a Met One Wind Direction Sensor at all sites.  The accuracy, as reported by the manufacturer, is to within plus/minus 5 degrees.  The wind direction sensors are calibrated annually by obtaining the fill scale return of the resistor and scaling this to the desired 360 degree output.  Additionally, the heading of the wind direction sensors are checked periodically each year by pointing the vane at aiming points for four compass points.  There are problems of note at these remote sites pertaining to wind speed and direction measurements.  The most significant off these are rime ice and freezing precipitation that can at best alter the aerodynamics of these sensors and possibly stop them completely.  No attempt was made to identify these periods in the data sets.  Prolonged periods of calm with wind speed reporting at the threshold velocity of 0.447 m/s and/or constant wind direction are very rare at these sites and should be considered indicators of these conditions.  However, we cannot be sure that a calm period did not occur since the sites were unmanned.  Rime ice and freezing precipitation can occur during any season but are most likely during the fall, late winter and early spring.  Sensors are cleaned at each site visit, but due to the remoteness of the sites, site visits are generally 1 to 3 months apart.  The second problem, specific to the wind sensors, is perching birds.  Since these sites are located in treeless tundra, large birds including ravens, rough leg hawks and snowy owls can damage vanes and anemometers by repeatedly perching on them.  This rarely caused data loss but may have slightly affected the accuracy of the wind vanes if they were bent.

Table 2a. Imnavait Research Watershed files.

Imnavait A Site

Meteorological

IA1985M.DAT

IA1986M.DAT

IA1987M.DAT

IA1988M.DAT

IA1989M.DAT

IA1990M.DAT

IA1991M.DAT

IA1992M.DAT

Continuing through 1993

Radiation

IA1985R.DAT

IA1986R.DAT

IA1987R.DAT

IA1988R.DAT

IA1989R.DAT

IA1990R.DAT

IA1991R.DAT

IA1992R.DAT

Continuing through 1993

Imnavait B Site

Meteorological

IB1986M.DAT

IB1987M.DAT

IB1988M.DAT

IB1989M.DAT

IB1990M.DAT

IB1991M.DAT

IB1992M.DAT

Continuing through 1999

Radiation

IB1986R.DAT

IB1987R.DAT

IB1988R.DAT

IB1989R.DAT

IB1990R.DAT

IB1991R.DAT

IB1992R.DAT

Continuing through 2007

Soil temperature

IB1986T.DAT

IB1987T.DAT

IB1988T.DAT

IB1989T.DAT

IB1990T.DAT

IB1991T.DAT

IB1992T.DAT

Continuing through 2007

Imnavait C Site

Soil temperature

and soil heat flux

IC1985T.DAT

IC1986T.DAT

IC1987T.DAT

IC1988T.DAT

IC1989T.DAT

IC1990T.DAT

IC1991T.DAT

IC1992T.DAT

Imnavait D Site

Soil temperature

ID1985T.DAT

ID1986T.DAT

ID1987T.DAT

ID1988T.DAT

ID1989T.DAT

ID1990T.DAT

ID1991T.DAT

ID1992T.DAT

Imnavait E Site

Soil temperature

IE1985T.DAT

IE1986T.DAT

IE1987T.DAT

IE1988T.DAT

IE1989T.DAT

IE1990T.DAT

IE1991T.DAT

IE1992T.DAT

Imnavait F Site

Soil temperature

IF1985T.DAT

IF1986T.DAT

IF1987T.DAT

IF1988T.DAT

IF1989T.DAT

IF1990T.DAT

IF1991T.DAT

IF1992T.DAT

Imnavait G Site

Soil temperature

IG1985T.DAT

IG1986T.DAT

IG1987T.DAT

IG1988T.DAT

IG1989T.DAT

IG1990T.DAT

IG1991T.DAT

IG1992T.DAT

Imnavait H Site

Streamflow

IH1985Q.DAT

IH1986Q.DAT

IH1987Q.DAT

IH1988Q.DAT

IH1989Q.DAT

IH1990Q.DAT

IH1991Q.DAT

IH1992Q.DAT

Continuing through 2007

Imnavait Ridge

IR1993T.DAT (8 Meter Profile)

Continuing through 2007

Imanvait Valley

IV1993T.DAT (8 Meter Profile)

Continuing through 2007

Imnavait S Site

Snow surveys

IS1985S.DAT

IS1986S.DAT

IS1987S.DAT

IS1988S.DAT

IS1989S.DAT

IS1990S.DAT

IS1991S.DAT

IS1992S.DAT

Imnavait W Site

Meteorological

IW1985M.DAT

IW1986M.DAT

IW1987M.DAT

IW1988M.DAT

IW1989M.DAT

IW1990M.DAT

IW1991M.DAT

IW1992M.DAT

## Table 2b. Remote sites files

Sagwon Hill Site

Meteorological

SH1986M.DAT

SH1987M.DAT

SH1988M.DAT

SH1989M.DAT

SH1990M.DAT

SH1991M.DAT

SH1992M.DAT

Continuing through 2007

Radiation

SH1987R.DAT

SH1988R.DAT

SH1989R.DAT

SH1990R.DAT

SH1991R.DAT

SH1992R.DAT

Continuing through 2007

Soil temperature

SH1986T.DAT

SH1987T.DAT

SH1988T.DAT

SH1989T.DAT

SH1990T.DAT

SH1991T.DAT

SH1992T.DAT

SH1993T1.DAT (original shallow profile)

Continuing through 2007

SH1993T2.DAT (10 meter deep profile)

Continuing through 2007

Sagwon Wyoming gage

SW1986M.DAT

SW1987M.DAT

SW1988M.DAT

SW1989M.DAT

SW1990M.DAT

SW1991M.DAT

SW1992M.DAT

Franklin Bluffs Site

Meteorological

FB1986M.DAT

FB1987M.DAT

FB1988M.DAT

FB1989M.DAT

FB1990M.DAT

FB1991M.DAT

FB1992M.DAT

Continuing through 2007

Radiation

FB1987R.DAT

FB1988R.DAT

FB1989R.DAT

FB1990R.DAT

FB1991R.DAT

FB1992R.DAT

Continuing through 2007

Soil temperature

FR1987T.DAT

FR1988T.DAT

FR989T.DAT

FR990T.DAT

FR1991T.DAT

FR1992T.DAT

FR1993T1.DAT (original shallow profile)

Continuing through 2007

FR1993T2.Dat (10 meter deep profile)

Continuing through 2007

Lower Kuparuk-Site

Meteorological

LK1992M.DAT

Continuing through 1995

Radiation

LK1992R.DAT

Continuing through 1995

Soil temperature

LK1992T.DAT

Continuing through 1995

Betty Pingo Site

Meterological

BM1995M.DAT continuing through 2007

Radiation

BM1995R.DAT continuing through 2007

Soil Temperature

Upland

BM2004TU.DAT continuing through 2007

Wetland

BM2004TW.DAT continuing through 2007

Upper Headwarter

UH1997M.DAT

Continuing through 2007

West Headwater

WH1997M.DAT

Continuing through 2007

North Headwater

NH1997M.DAT

Continuing through 2007

East Headwater

EH1997M.DAT

Continuing through 2007

Green Cabin Lake

GL1997M.DAT

Continuing through 2007

## AIR TEMPERATURE AND RELATIVE HUMIDITY

Air temperature and relative humidity were measured using a Campbell Scientific Model 207 Temperature and Relative Humidity Probe. The relative humidity component utilizes a Phys-Chemical Research Corporation PCRC humidity transducer.  These probes were housed in a self-aspirating radiation shield and are used to measure temperature and relative humidity at all sites.  The reported temperature operating range is -33 to +48 degrees C with a worst case accuracy of plus/minus 0.4 degrees C and typically an accuracy of plus/minus 0.2 degrees C, and plus/minus 1 degree C from -33 degrees C to -40 degrees C.  The relative humidity operating range is 12 to 100 percent with an accuracy of plus/minus 5 percent.  A Campbell Scientific model 105T type T thermocouple was also used at the Imnavait B site.  This thermocouple's calibrated range is -78 degrees to 50 degrees C, plus/minus 0.2 degrees C.

In 1995 HMP35C or HMP45C Temperature Relative Humidity Sensors were added to each main site at the 10 meter height.

In 2000 the Model 207 Probe sensors were replaced with CSI Model 500 sensors.

In 2004 all of the CSI Model 500 T/RH sensors were replace due to corrosion problems in the sensor lead.

As with the wind speed above, rime ice accumulations can affect the air temperature and especially the relative humidity reading obtained. This is caused by insulating the sensors within the radiation shield and isolating them from ambient conditions.  Given these conditions, air temperature readings would be affected slightly in the time required to respond to changes in the ambient air temperature.  Also, relative humidity would be greatly affected by being isolated from the ambient conditions, recorded humidities would be related to the vapor pressure of the surface of the rime ice adhering to the radiation shield and wire mesh inner enclosure surrounding the relative humidity sensor and not indicative of the true ambient conditions.

## SOIL TEMPERATURE

Soil temperatures were measured at all sites using YSI model 44007 Thermistors and 100 K ohm precision resistors. These thermistors are rated at plus/minus 0.2 degrees C from 0 to 80 degrees C.  The accuracy declines below 0 degrees C to plus/minus 0.3 degrees C at -25 degrees C, plus/minus 0.4 degrees C at -40 degrees C and plus/minus 1.0 degree C at -80 degrees C.

## RADIATION

Radiation instruments were installed in the spring usually during March or April and were taken down in the fall (late August or September).  Since rime ice, snowfall and freezing precipitation can obscure the sensors in these instruments, values reported during periods of below freezing air temperature should be closely scrutinized.  Reported radiation values during winter, early spring and fall should be considered qualitative and not quantitative.  The following radiation components were measured: incoming and reflected shortwave radiation, atmospheric and terrestrial longwave radiation, photosynthetically active radiation and net radiation.  Radiometer calibrations are checked locally each year by comparison to the output of an instrument of known precision. Every 5 years the radiometers are sent to Eppley Labs for reconditioning and recalibration.  All radiometers in use before 1988 were calibrated in March of 1989.  All instruments were leveled at each site visit.  Although the mounts were made as solid as possible, thawing and refreezing of the active layer soils above the permafrost did cause occasional shifting of the sensors between site visits.

## Net Radiation

Net absorbed radiation was measured with a Swissteco model S-1 Net Radiometer at all sites from 1985/1986 through 1992. except the Lower Kuparuk site where a REBS Q6 Net Radiometer was used.  In 1993, all Swissteco net radiometers were replace with REBS Q^ Net Radiometers.  In 1998 all of the REBS Q6 net radiometers were upgraded to REBS Q7.1 net radiometers at all sites measuring net radiation.  The operating range of the Swissteco instrument is 0.3 to 60 M; the accuracy is reported as plus/minus 2.5 percent.  The Radiation and Energy Balance Systems (REBS) Q6 Net Radiometer's spectral response range is reported by the manufacturer as 0.25 to 60 uM, the calibrated accuracy of this instrument was not reported by the manufacturer.  The REBS Q7.1 radiometers have independently calibrated atmospheric and terrestrial sensors and measure the same spectrum.

Net radiation components, total hemispheric terrestrial and atmospheric radiation, were also measured using a Weathertronics Pyrradiometer at the Imnavait A site.  This sensor produces two outputs, the total incoming and total emitted or reflected radiation, the difference being the net absorbed radiation.  The accuracy of this instrument was reported to be within 2 percent.

## Shortwave Radiation

Incident and reflected shortwave radiation were measured with a Weathertronics Albedometer at Imnavait A site.  The spectral range of this sensor is 0.3 to 3 microns, which excludes the terrestrial longwave component.  The accuracy of this sensor is reported to be plus/minus 1 percent and the cosine response is less than 1 percent when the sun angle is within 0 to 70 degrees of perpendicular of the sensor plane.

Incident shortwave radiation was also measured using an Eppley model PSP Precision Spectral Pyranometer at Imnavait A site. This type of instrument was also used to measure incident and reflected shortwave radiation at Franklin Bluffs,Sagwon, and Lower Kuparuk sites.  An Eppley Spectral Precision Pyranometer fitted with an RG8 dark red filter was used to measure photosynthetically active radiation between 0.700 and 2.800 microns at the Imnavait A site.  This instrument has a reported spectral range of 0.285 to 2.800 microns, and a reported accuracy of plus/minus 1 percent in the range of values encountered.  The cosine response of this instrument is plus/minus 1 percent between 0 and 70 degrees and plus/minus 3 percent between 70 degrees and 80 degrees zenith angle.

Eppley model 8-48 Black and White Pyranometers were used to measure incident and reflected solar radiation at the Imnavait B site.  This instrument has a reported spectral range of 0.28 to 2.800 microns, and a reported accuracy of plus/minus 1.5 percent in the range of values encountered.  Cosine response is reported as plus/minus 2 percent from normalization for angles of 0 degrees to 70 degrees and plus/minus 5 percent.

## Longwave Radiation

Eppley model PIR Precision Infrared Pyrgeometers were used to measure longwave radiation, both terrestrial and atmospheric, at all sites. The spectral range of this type of instrument is 4 to 50 M, and the accuracy is reported as plus/minus 1 percent between 0 and 700 W/m2.

## STREAMFLOW

Stream discharge was estimated from stage data recorded by Leupold Steven's F1 water level recorders within an H type flume.  A stage discharge relationship was developed from discharge measurements made with Price AA (Gurley) and Pygmy cup type current meters, Montedoro Whitney electromagnetic current meters and Sontek Accoutic Dopler current meters using standard USGS stream cross section techniques to estimate stream discharge from the recorded stage data.

## SNOWPACK

Snowpack depth and water equivalent were measured using an Adirondak snow sampler, CRREL snow depth probe and manual graduated snow depth probes .  1985 to 1993 reported values are averages of at least 10 depth and density measurements. Beginning in 1994 values represent densities from 5 snow cores and 50 depths measured over a 50 meter transect.

Table 2.

North Slope site status, identity code and location.

Site	Name			Latitude		Longitude		Elevation

Imnavait Trailer (home)		68° 37' 03.6" N		149° 18' 15.1" W

Imnavait Basin (IB)		68° 36' 58.6" N		149° 18' 13.0" W	937 meters

Imnavait Ridge (IR)		68° 37' 27.9" N		149° 19' 22.3" W

Imnavait Valley (IV)		68° 37' 02.7" N		149° 19' 02.3" W			Imnavait Flume (IH)		68° 37' 02.1" N		149° 19' 08.1" W	881 meters

Imnavait Water Track 7 (IT)*

Imnavait Plot1 (ID)*		68° 36' 36" N		149° 18' 11" W

Imnavait Plot2 (IE)*		68° 36' 36" N		149° 18' 12" W

Upper Kuparuk m,r,s (UK)	68° 38' 24.5" N		149° 24' 23.4" W	774 meters

Upper Kuparuk River q (UK)	68° 38' 35" N		149° 24' 15" W		747 meters

North Headwater (NH)		68° 36' 04.8" N		149° 25' 52.8" W

East Headwater (EH)		68° 34' 7.6" N		149° 18' 32.4" W

West Headwater (WH)		68° 33' 48.0" N		149° 24' 30.0" W

Green Cabin Lake (GL)		68° 32' 01.0" N		149° 13' 47.4" W

Upper Headwater (UH)		68° 31' 19.8" N		149° 20' 18.0" W				West Kuparuk (WK)		69° 25' 34.3" N		150° 20' 25.3" W	158 meters

Sagwon (SH)			69° 25' 27.5" N		148° 41' 45.1" W	299 meters		Franklin Bluffs (FR)		69° 53’ 31.8” N		148° 46’ 4.8” W		77.7 meters

Kuparuk Deadhorse (KD)*	70° 17' N 		148° 58' W

[aka Lower Kuparuk (LK)]

Betty Wetland/Met (BM)		70° 16' 46.3" N		148° 53' 44.5" W	11.6 meters

Betty Upland (BU)		70° 16' 46.9" N		148° 53' 46.5" W

Betty TDR (BT)			70° 16' 46.7" N		148° 53' 46" W

West Dock (WD)		70° 22' 50" N		148° 33' 39" W		7.6 meters

NOTE: Decommissioned or abandoned site designated by *.

rg 5/17/01

REFERENCES

Brown, J. and R.L. Berg, (eds.).  1980.  Environmental engineering and ecological baseline investigations along the Yukon River-Prudhoe Bay Haul Road.  U.S. Army CRREL Report 80-19.  187 p.

Everett, K.R. and B. Ostendorf. 1988.  Hydrology and geochemistry of a small drainage basin in upland tundra, northern Alaska. Proceedings, 5th International  Conference on Permafrost, K. Senneset (Ed), 2-5 August 1988.  Trondheim, Norway, Tapir Publishers, Vol. 1, pp. 574-579.

Everett, K.R.  1980.  Soils and Mapping. In - Environmental Engineering and Ecological Baseline Investigations along the Yukon River - Prudhoe Bay Haul Road. J. Brown and R.L. Berg (Eds.) CRREL Report No. 80-19. Cold Regions Research and Engineering Laboratory.  U.S. Army Corps of Engineers, Hanover, New Hampshire, pp. 48-52.

Hinzman, L.D., Kane, D.L., Gieck, R.E. and Everett, K.R.  1991.  Hydrologic and thermal properties of the active layer in the Alaskan Arctic. Cold Regions Science and Technology, Vol. 19, pp. 95-110.

Hinzman, L.D. and Kane, D.L.  1991.  Snow hydrology of a headwater Arctic basin 2. Conceptual analysis and computer modeling.  Water Resources Research, Vol. 27(6), pp. 1111-1121.

Hinzman, L.D., G. Wendler, R.E. Gieck, and D.L. Kane. 1992.  Snowmelt at a small Alaskan arctic watershed 1. energy related rocesses.  Northern Research Basins Conference. Whitehorse, Northwest Territories, Canada.

Kane, D.L. and Hinzman, L.D.  1988.  Permafrost hydrology of a small arctic Watershed. Proceedings Fifth International Conference on Permafrost, K. Senneset (ed.), Trondheim, Norway, Tapir, pp. 590-595.

Kane, D.L., Hinzman, L.D., Benson, C.S. and Everett, K.R.  1989.  Hydrology of Imnavait Creek, an arctic watershed. Holarctic Ecology, Vol. 12, pp. 262-269.

Kane, D.L., Gieck, R.E. and Hinzman, L.D. 1990.  Evapotranspiration from a small Alaskan arctic watershed.  Nordic Hydrology, Vol. 21(4/5), pp. 253-272.

Kane, D.L., Hinzman, L.D., Benson, C.S. and Liston, G.E. 1991a.  Snow hydrology of a headwater arctic basin 1. Physical measurements and process studies. Water Resources Research, Vol. 27(6), pp. 1099-1109.

Kane, D. L., Hinzman, L. D. and Zarling, J. P. 1991b.  Thermal response of the active layer in a permafrost environment to climatic warming. Cold Regions Science and Technology, Vol. 19, pp. 111-122.

Komarkova, V. and P.J. Webber. 1980.  Vegetation, In - Environmental Engineering and Ecological Baseline Investigations along the Yukon River - Prudhoe Bay Haul Road. J. Brown and R. L. Berg (Editors).  CRREL Report No. 80-19.  Cold Regions Research and Engineering Laboratory, U.S. Army Corps of Engineers, Hanover, New Hampshire, p. 37-42.

Rieger, S., D.B. Schoephorster, and C.E. Furbush. 1979.  Exploratory soil survey of Alaska.  U.S.D.A. Soil Conservation Service.  Washington D.C. 213 p.

Walker, M.D., D.A. Walker and K.R. Everett.  1989.  Wetland soils and vegetation, Arctic Foothills, Alaska. U.S. Fish and Wildlife Service. Biological Report 89(7), 89 p.